## Slide 1: Edge / Boundary Detection

## Slide 2: Edge detection
Goal: Identify sudden changes (discontinuities) in an image
  Intuitively, most semantic and shape information from the image can be encoded in the edges
  More compact than pixels
Ideal: artist’s line drawing (but artist is also using object-level knowledge)
Source: D. Lowe

## Slide 3: Why do we care about edges?
Extract information, recognize objects
Recover geometry and viewpoint
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 4: Origin of Edges
Edges are caused by a variety of factors
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity
Source: Steve Seitz

## Slide 5: Closeup of edges
Source: D. Hoiem

## Slide 6: Closeup of edges
Source: D. Hoiem

## Slide 7: Closeup of edges
Source: D. Hoiem

## Slide 8: Closeup of edges
Source: D. Hoiem

## Slide 9: Characterizing edges
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative

## Slide 10: Intensity profile
Source: D. Hoiem

## Slide 11: With a little Gaussian noise
Gradient
Source: D. Hoiem

## Slide 12: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?
Source: S. Seitz
Notes: How to fix?

## Slide 13: Effects of noise
Difference filters respond strongly to noise
  Image noise results in pixels that look very different from their neighbors
  Generally, the larger the noise the stronger the response
What can we do about it?
Source: D. Forsyth

## Slide 14: Solution: smooth first
To find edges, look for peaks in
f
g
f * g
Source: S. Seitz

## Slide 15: Derivative theorem of convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz

## Slide 16: Derivative of Gaussian filter
* [1 -1] =
Notes: Is this filter separable?

## Slide 17: Laplacian of Gaussian
Consider
Laplacian of Gaussian
operator
Where is the edge?
Zero-crossings of bottom graph

## Slide 18: 2D edge detection filters
is the Laplacian operator:
Laplacian of Gaussian
Gaussian
derivative of Gaussian

## Slide 19: Tradeoff btw smoothing and localization
Smoothed derivative removes noise, but blurs edge. Also finds edges at different “scales”.
1 pixel
3 pixels
7 pixels
Source: D. Forsyth

## Slide 20: Implementation issues
The gradient magnitude is large along a thick “trail” or “ridge,” so how do we identify the actual edge points?
How do we link the edge points to form curves?
Source: D. Forsyth
Notes: Figures show gradient magnitude of zebra at two different scales

## Slide 21: Designing an edge detector
Criteria for a good edge detector:
  Good detection: the optimal detector should find all real edges, ignoring noise or other artifacts
  Good localization
    the edges detected must be as close as possible to the true edges
    the detector must return one point only for each true edge point
Cues of edge detection
  Differences in color, intensity, or texture across the boundary
  Continuity and closure
  High-level knowledge
Source: L. Fei-Fei

## Slide 22: Canny edge detector
This is probably the most widely used edge detector in computer vision
Theoretical model: step-edges corrupted by additive Gaussian noise
Canny has shown that the first derivative of the Gaussian closely approximates the operator that optimizes the product of signal-to-noise ratio and localization
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.
Source: L. Fei-Fei

## Slide 23: Note about Matlab’s Canny detector
Small errors in implementation
  Gaussian function not properly normalized
  First filters with a Gaussian, then a difference of Gaussian (equivalent to filtering with a larger Gaussian and taking difference)

## Slide 24: Example
original image (Lena)

## Slide 25: Derivative of Gaussian filter
x-direction
y-direction

## Slide 26: Compute Gradients (DoG)
X-Derivative of Gaussian
Y-Derivative of Gaussian
Gradient Magnitude

## Slide 27: Get Orientation at Each Pixel
Threshold at minimum level
Get orientation
theta = atan2(gy, gx)

## Slide 28: Non-maximum suppression for each orientation
At q, we have a maximum if the value is larger than those at both p and at r. Interpolate to get these values.
Source: D. Forsyth

## Slide 29: Edge linking
Assume the marked point is an edge point. Then we construct the tangent to the edge curve (which is normal to the gradient at that point) and use this to predict the next points (here either r or s).
Source: D. Forsyth

## Slide 30: Sidebar: Bilinear Interpolation
http://en.wikipedia.org/wiki/Bilinear_interpolation

## Slide 31: Sidebar: Interpolation options
imx2 = imresize(im, 2, interpolation_type)
‘nearest’
  Copy value from nearest known
  Very fast but creates blocky edges
‘bilinear’
  Weighted average from four nearest known pixels
  Fast and reasonable results
‘bicubic’ (default)
  Non-linear smoothing over larger area (4x4)
  Slower, visually appealing, may create negative pixel values
Examples from http://en.wikipedia.org/wiki/Bicubic_interpolation

## Slide 32: Before Non-max Suppression

## Slide 33: After non-max suppression

## Slide 34: Before Non-max Suppression

## Slide 35: After non-max suppression

## Slide 36: Hysteresis thresholding
Threshold at low/high levels to get weak/strong edge pixels
Do connected components, starting from strong edge pixels

## Slide 37: Hysteresis thresholding
Check that maximum value of gradient value is sufficiently large
  drop-outs? use hysteresis
    use a high threshold to start edge curves and a low threshold to continue them.
Source: S. Seitz

## Slide 38: Final Canny Edges

## Slide 39: Canny edge detector
Filter image with x, y derivatives of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression:
  Thin multi-pixel wide “ridges” down to single pixel width
Thresholding and linking (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
MATLAB: edge(image, ‘canny’)
OpenCV: Canny( src, dst, lowThreshold, highTreshold, kernel_size )
It needs Gaussian, first
Source: D. Lowe, L. Fei-Fei

## Slide 40: Effect of σ (Gaussian kernel spread/size)
Canny with
Canny with
original
The choice of σ depends on desired behavior
  large σ detects large scale edges
  small σ detects fine features
Source: S. Seitz

## Slide 41: Lines

## Slide 42: Edges are not lines

## Slide 43: Finding lines in an image
Option 1:
  Search for the line at every possible position/orientation
  What is the cost of this operation?
Option 2:
  Use a voting scheme: Hough transform

## Slide 44: The basic idea
Each straight line in this image can be described by an equation
Each white point if considered in isolation could lie on an infinite number of straight lines

## Slide 45: The basic idea
Each straight line in this image can be described by an equation
Each white point if considered in isolation could lie on an infinite number of straight lines

## Slide 46: The basic idea
Each straight line in this image can be described by an equation
Each white point if considered in isolation could lie on an infinite number of straight lines
In the Hough transform each point votes for every line it could be on
The lines with the most votes win

## Slide 47: How do we represent lines?
Conventional representation
  A line is parameterized by and
  Problems?
More general way
  A line is represented by , , and
  Problem: , , and are “homogenous”
Better way
  Normalization:
  Now we can represent a line with

## Slide 48: How do we represent lines?
Here we will represent the yellow line by
In other words we define it using
  a line from an agreed origin
  of length
  at angle to the horizontal

## Slide 49: Hough space
Since we can use to represent any line in the image space
We can represent any line in the image space as a point in the plane defined by
This is called Hough space

## Slide 51: How does a point in image space vote?
For a
For another

## Slide 52: Magnified

## Slide 53: How do multiple points prefer one line?
One point in image space
  corresponds to a sinusoidal curve in image space
Two points
  correspond to two curves in Hough space
The intersection of those two curves
  “two votes”
This intersection represents
  the straight line in image space that passes through both points

## Slide 54: Magnified

## Slide 55: Hough Transform
Create and for all possible lines
Create an array A indexed by and and set to zero
for each edge point (x,y)
for each angle
= x*cos()+ y*sin()
H[, ] += 1
end
end
where A > Threshold return a line

## Slide 56: A simple example

## Slide 57: Extensions
Extension 1: Use the image gradient
for each edge point (x,y)
compute unique (,) based on image gradient at (x,y)
H[, ] += 1
end
What’s the running time measured in votes?
Extension 2
  give more votes for stronger edges
Extension 3
  change the sampling of (d, ) to give more/less resolution

## Slide 58: Circle Hough Transform
  for each edge point (x,y)
    for all possible r
      compute a and b
      H[a,b,r]+=1
  Find the value(s) of (a, b, r) where H[a, b, r] is maximum
  The detected circle in the image is given by

## Slide 59: Assignment #2
Counting Coins
  Detect edges of coins
  Find a circle fitting each coin
  Draw the circles on the image
  Print the number of coins

## Slide 60: Challenge #1
Business card rectification
  Find edges
  Find important lines
  Compute four corners
  Get the 2D perspective transform
    onto some rectangle
  Warp the input image